## Slide 1: West Valley Nuclear Waste Site Erosion Modeling Update 26-27 March 2024
New York State Professional Geological Services PLLC
Thomas J. Morahan, PG

## Slide 2: Background
Team
Thomas J. Morahan, P.G.
Raymond C. Vaughan, Ph.D., P.G.
Shannon Seneca, Ph.D.
Jason Hanania
Kit Cross

## Slide 3
WEST VALLEY NUCLEAR WASTE SITE
Operated as a nuclear reprocessing plant (1965 to 1972) and burial site for radioactive waste (1963 to 1975). No new waste has arrived at the site since 1975. Maintenance and remedial work since then.
The site is about 6 square miles of state-owned land in Ashford. Most of this is buffer zone surrounding about 200 acres occupied by the two unlined burial grounds (SDA and NDA) and other facilities such as the reprocessing plant that’s now being demolished.
SDA = State-Licensed Disposal Area (15 acres), containing about 2.4 million cubic feet of waste
NDA = NRC-Licensed Disposal Area (8 acres)
WEST VALLEY NUCLEAR WASTE SITE

## Slide 4
WEST VALLEY NUCLEAR WASTE SITE
A site-specific federal law (the West Valley Demonstration Project Act) was passed in 1980 to solidify 600,000 gallons of high-level liquid waste (HLLW) and clean up part of the site. DOE and NYSERDA have safely vitrified the HLLW.
This was done by mixing radioactive material from the HLLW into melted borosilicate glass and pouring the hot glass mixture into stainless steel canisters, in order to make highly radioactive glass that is physically stable and resistant to leaching.
Vitrified waste is still onsite but relatively safely stored – must eventually be removed.
WEST VALLEY NUCLEAR WASTE SITE

## Slide 5
No decision yet on whether the SDA and NDA burial grounds will be dug up and removed. Decision may be made in about 2 years?
Franks Creek and Erdman Brook run alongside both burial grounds, and these two creeks are actively eroding.
Both creeks are becoming deeper and wider as they erode. At some point in the future they will cut into the sides of the burial grounds and start carrying wastes downstream – but how soon?
A 1996 prediction by DOE and NYSERDA showed severe future erosion. Their 2005-2010 prediction showed much less erosion. Which one to trust?
WEST VALLEY NUCLEAR WASTE SITE

## Slide 6
Map adapted from Bergeron, USGS, 1983

## Slide 7
Map adapted from Bergeron, USGS, 1983

## Slide 9: Town of Ashford Hydro/Erosion Model Objectives
Develop a Model to Help Estimate
Long-term Erosion Scenarios
  10,000 Years
  Recognizing Cohesive Sediments
The Effects of Climate Change
  Rainfall
  Snowmelt

## Slide 10: Choice of a Model To Use
Model Options
United States Environmental Protection Agency (USEPA)
  Advanced Geospatial Watershed Analysis (AGWA) Model
USDOE / Neptune
  Hydrologic Models
    WGEN - Weather
    HELP - Landfill Performance
    FEHM - Groundwater Movement
    SWAT - Water and Sediment Transport
  Probabilistic Performance Assessment
    GoldSim - Integrated Transport Model
United States Army Corps of Engineers (USACE) Hydraulic Engineering Center (HEC)
  Hydrologic Modeling System (HMS)
  River Analysis System (RAS)
Model Choice
United States Army Corps of Engineers (USACE) Hydraulic Engineering Center (HEC) River Analysis System (RAS)
HEC-RAS is a robust, well-documented model that best supports volumetric sediment transport

## Slide 11: HEC RAS Model Development
Geometry
Flow
Sediment
Plan
  Allows Different Model Assumptions
2D Model Option

## Slide 12: HEC RAS Geometry
NYSERDA LiDAR Data
  Digital Elevation Model
Plus
  Land Use
  Cover
  Soil Types

## Slide 13: HEC RAS Geometry
2D Mesh
  For Computations
Cross Sections of Stream Bottoms
  Franks Creek
  Erdman Brook
  Quarry Creek

## Slide 14: HEC RAS Flow
Current Hydro Model
  Unsteady Flow
Quasi Unsteady Flow
  Best for Sediment Transport
  More Stable
  Handles Cohesive Sediments
Requires Additional Data
  Shear Stress
  Grain Size Distribution
Conceptual Site Model
  Erosion Exposes Different Geology
  Fence Diagram from Boring Logs
  Transects Under Development
2009 Storm - Buttermilk Creek
  Demonstrated Cohesive Sediment Complexity
  Dessication of Till Fractures

## Slide 15: Geological Cross Section

## Slide 16: Current Flow Model Showing 2-year Storm Event

## Slide 17: Current Flow Model Showing 500-year Storm Event

## Slide 18: Current Flow Model Showing 24 Hour Event Water Depth
Year
0
5
25
50
100
500

## Slide 19: Sediment mass removal Recent Storm Events on Buttermilk Creek Validate Flows

## Slide 20: Next Steps
Develop Quasi Unsteady Flow Model
  Transport Parameters (e.g. shear stress, grain size)
  Validate Storm Event Data
Update Model with Climate Change Data
  Climate Change Estimates Using Atlas 14 or Other Data
  Snowmelt Considerations
Develop Sediment Erosion Data
  Cumulative Volume of Sediment Removed
  Estimate Future Topography
Develop Report

## Slide 21: Questions
Thomas J. Morahan, P.G.
Buffalo, NY
716 (374) 0640